## Slide 1: Processor Customization Using TCE Quick Walkthrough Screencast
By Aleksi Tervo and
Pekka Jääskeläinen of
Customized Parallel Computing group ,
Tampere University of Technology, Finland
http://cpc.cs.tut.fi
Updated on 2018-06-27

## Slide 2: Defining the Application Source Code

## Slide 3: Example App: CRC32 Checksum
Notes: Basic Cyclic Redundancy Check application
Used to calculate CRC-32 for a short 10-character string

## Slide 4: Defining a Starting Point Architecture

## Slide 5: Let’s Start with a Minimal TTA Supported by the TCE Compiler
Notes: Minimal architecture: one LSU, one simple ALU, 5 registers

## Slide 6: Compilation and Instruction-Set Simulation

## Slide 7: Simulation
Notes: 12s

## Slide 8: Identifying the Bottlenecks
Starting point instruction cycles: 2315

## Slide 9: Locating Bottlenecks
Notes: Simulation shows us LSU is seeing high utilization
Caused by register file spilling
 Increase RF size

## Slide 10: Adding Registers to Reduce Spills
Notes: Simulation shows us LSU is seeing high utilization
Caused by register file spilling
Increase RF size

## Slide 11: Simulation
Notes: Memory operations significantly cut
Cycle count from 2315 to 990 -> 58% decrease

## Slide 12: Interconnect network
Current cycle count is 990 (down from 2315)
Currently, the machine only has one bus
  Moving the data to start an ALU operation takes two cycles!
Adding a second bus should increase performance considerably

## Slide 13: Adding a Second Bus
Notes: 6s

## Slide 14: Simulation
Cycle count from 990 to 581 -> 42% decrease from previous architecture
Notes: Cycle count from 990 to 581 -> 42% decrease from previous architecture.

## Slide 15: Adding a Custom Operation
Current instruction cycles: 581

## Slide 16: Add an Operation Semantics Definition with Operation Set Editor
Notes: 17s

## Slide 17: Add a Function Unit with the Custom Operation to the Architecture
Notes: 31s

## Slide 18: Modify Code to Call the Complex Custom Operation via Autogenerated Intrinsics

## Slide 19: Simulation
Cycle count from 581 to 139 -> 77% decrease
Notes: Simulation supports custom operation -> can verify code correctness from result
Cycle count from 581 to 139 -> 77% decrease
Final cycle count is 1/16 of original

## Slide 20: RTL Implementation
Notes: In order to generate a processor, we need to describe the custom FU we added in RTL
(There’s some automation availabel for simple FUs)
Main logic of the function unit is very simple:
When processor is running and operation is loaded,
Write result of selected operation to output register

## Slide 21: Add a Function Unit Implementation to a Hardware Database

## Slide 22: Add FU to HDB
Notes: Specify FU in hdbeditor:
Port names, generics, RTL files and compilation order i.e. the info required to instantiate the component

## Slide 23: Add FU to HDB
Notes: Resulting database entry

## Slide 24: Select Implementations for Architecture Components
Notes: Select implementations from the default HDB and the one containing custom FU

## Slide 25: Generating the VHDL or Verilog RTL

## Slide 26: Finally: Generate the RTL
Notes: All that’s left to do for a working core is to connect memories to the core interfaces
There are automatic integrators for FPGAs